## Slide 1
SIG-TFN: Welcome
Guy Roberts
Senior Network Architect
SIG-TFN Amsterdam
16-17/10/2024

## Slide 2
Time (CEST) | Room L1.07, Lab42 building
12:00 - 13:00 | Arrival & Lunch at Café Neo (self-paid)
13:30 - 13:45 | Welcome and introduction - Guy Roberts, GÉANT
13:45 - 14:15 | SIG-TFN Overview - Guy Roberts, GÉANT
14:15 - 14:45 | NPL time frequency links - Jacques-Olivier Gaudron, NPL
14:45 - 15:15 | Coffee break
15:15-16:15 | Technical Working Group - Jeroen Koelemeij, Free University of Amsterdam Design of the Lille-Brussels-Amsterdam-Braunschweig link
16:15 - 16:45 | Optical clocks in Amsterdam (iqClock & QDNL clock project) - Florian Schreck, UvA https://www.iqclock.eu/university-of-amsterdam.html
17:00 - 18:15 | Lab tour - UvA
18:30 | Informal group dinner at Cafe Restaurant Polder (on UvA campus). (self-paid)
Agenda: Wednesday

## Slide 3
Agenda: Thursday
Time (CEST) | Room G3.10, Science Park G
09:00 - 09:30 | CESNET to discuss national WR network - Josef Vojtech & Vladimir Smotlacha, CESNET
09:30 - 10:00 | White Rabbit Status and Plans - Maciej Lipinski, CERN
10:00 - 10:30 | Pathfinder update - Krzysztof Turza, PSNC
10:30 - 11:00 | Coffee break
11:00 - 11:30 | Italian Quantum Backbone: time and frequency metrology, quantum communications, and sensing over optical fibers - Davide Calonico, INRIM
11:30 - 12:00 | EC discussion on future funding possibilities - Lukasz Bonenberg, EC JRC
12:00 - 12:30 | Sustainability Working Group - Richard Lui, GÉANT Update and discussion.
12:30 - 12:45 | Wrap up & closing - Guy Roberts, GÉANT
13:00 | Lunch at Café Neo (self-paid)

## Slide 4
C-TFN: an update
Guy Roberts
Senior Network Architect
SIG-TFN Amsterdam
16-17/10/2024

## Slide 5: Timeline
2014-16
2017-19
2020-23
Feb 2024
June2024
REFIMEVE+ frequency links. MuQuans founded
NPL-SYRTE fibre link built
CLONETS project
CLONETS-Design Study
CERN workshop
Launch SIG-TFN
2012

## Slide 6: SIG-TFN
Why do we need a new Special Interest Group?
New scientific community of metrology
SIG-TFN brings together NRENs and the science of accurate time
Strong interest: 100 subscribers to sig-tfn@lists.geant.org

## Slide 7: SIG-TFN
GÉANT is the coordinator of SIG-TFN
Web page: https://community.geant.org/sig-tfn/
Steering committee
  Guy Roberts (GÉANT)
  Paolo Bolletta (GARR)
  Josef Vojtech (CESNET)
  Krzyztof Turza (PSNC)
  Jacques-Oliver Gaudron (NPL)
  Christian Chardonnet (REFIMEVE)
  Coordinators: Domenico Vicinanza (GÉANT) and Nadelina Sandu (GÉANT)
There are two working groups within the SIG-TFN:
  T/F Sustainability (led by Richard Lui)
  C-TFN technical specification (Led by Guy Roberts)

## Slide 8: C-TFN sustainability working group
Team
  Richard Lui (WG leader)
  Raphaël Marion
  Christian Chardonnet
  Wojbor Bogacki
  Christian Lisdat
  Davide Calonico
Objectives
Investigate a path to sustainability of the CLONETS-DS C-TFN, both for GÉANT and for participating NRENs and NMIs.
Carry out cost modelling to identify the extent of the future funding needs for fibre and flywheels.
Shepard funding through governance of GN5-2
Engage EURAMET, NRENs, GÉANT and the European Commission to find solutions to long-term funding.

## Slide 9: C-TFN technical specification working group
Team
  Guy Roberts (WG leader)
  Jochen Kronjaeger
  Raphaël Marion
  Krzysztof Turza
  Jacques-Olivier Gaudron
Objectives
Expand on the CLONETS-DS architecture and integrate lessons learnt from PTB-PSNC pathfinder.
Investigate if tiers of flywheel performance are needed e.g NMI flywheel, NREN flywheel, etc.
Prepare a C-TFN architecture
Prepare a technical specification for the C-TFN flywheels.
Prepare a technical specification for the GÉANT cross-border fibre links.

## Slide 10: Summary of use cases
Support the redefinition of the SI second being carried out between now and 2030+ by NPL, PTB, Syrte and INRIM and other NMIs.
Perform fundamental physics research e.g. gravity wave experiments.
Supplement GNSS with a fibre network to increase reliability of time distribution
Support European-wide commercial services such as very accurate time stamps for banks to validate high-frequency trading.

## Slide 11: Services as an overlay to fibre links
GEANT C-TFN
NREN C-TFN
flywheel / frequency comb
NMI
NMIs
Build, own and operate the T/F equipment:
  Flywheels, counters, frequency combs
Retain ownership of time/frequency
Generate and measure time/frequency
Terminate T/F services
Transport of T/F services
Time/freq. service overlay
RLS
NMI access point
GEANT, NRENs
build, own and operate transport links:
  fibre, amplifiers, access points, intermediate RLS
Provide a service to NMIs to carry T/F services
RLS
Ch. 45
NMI access point
WR
ELSTAB
Ch. 46
Ch. 44
flywheel / frequency comb
NMI
RLS
Ch. 45
WR
ELSTAB
Ch. 46
Ch. 44
Frequency service instance
White Rabbit service instance
ELSTAB service instance

## Slide 12: How things stand today
NMI Frequency reference
Hut for housing RLS
Research institute
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
VSL
Delft
UvA
Innsbruck
Lithuania
Frequency network:
Green links built by NRENs in collaboration with national NMIs
Blue links built by local NMIs/researchers
NMIs:
Four big NMIs are involved in redefining the SI second highlighted in red
Wroclav
Hradec
Kralove

## Slide 13: What is missing?
NMI Frequency reference
Hut for housing RLS
Research institute
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
UvA
Innsbruck
Lithuania
Missing:
National based networks need to be interconnected
Eastern and Western islands of frequency services are not linked
A full ring/mesh of the big four NMIs will enable them to complete definition of the SI second
Link will also be needed to Nordics, SE and SW Europe as they develop Optical clocks
Wroclav
Hradec
Kralove
VSL
Delft

## Slide 14: Proposed solution
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
UvA
Innsbruck
Lithuania
Solution:
Red lines are proposed for GN5-2
These will interconnect national ‘islands’ of frequency networks
Support redefinition of the SI second
Primary users are national frequency reference providers
Secondary users are research institutes that connect via their national frequency provider
Wroclav
Hradec
Kralove
NMI Frequency reference
Hut for housing RLS
Research institute
VSL
Delft

## Slide 15: Proposed solution
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
UvA
Innsbruck
Lithuania
Solution:
Ring supports the four big NMIs that are part of the campaign for redefinition of the SI second
Wroclav
Hradec
Kralove
NMI Frequency reference
Hut for housing RLS
Research institute
VSL
Delft

## Slide 16: Pathfinder system
First proof-of-concept link for the CLONETS C-TFN
The purpose is to prove both frequency and time transfer
The system was successfully installed on the 23rd of Sept
Uses equipment from PIK Time Systems
Bi-directional amp
Regenerator laser station
ELSTAB

## Slide 17
Pathfinder validation results

## Slide 18: TimeMap for pathfinder
GEANT WP6 is adapting TimeMap software to support the Pathfinder
Link state and beat power are reported for each end of the link
Investigating adding frequency counter measurements

## Slide 19: WDM wavelength plan for TF signals (lambdas TBD)
ELSTAB Tx
ELSTAB Rx
WR Tx
WR Rx
MUX
Optical fiber b
WR Tx Cal
WR Rx Cal
CH44 ultrastable
optical carrier
ELSTAB Rx
ELSTAB Tx
WR Rx
WR Tx
WR Rx Cal
WR Tx Cal
CH44 ultrastable
optical carrier
MUX
ELSTAB Rx
ELSTAB Tx
WR Rx
WR Tx
MUX
Optical fiber a
WR Rx Cal
WR Tx Cal
CH44 ultrastable
optical carrier
ELSTAB Tx
ELSTAB Rx
WR Tx
WR Rx
WR Tx Cal
WR Rx Cal
CH44 ultrastable
optical carrier
MUX
Fiber pair
Time Grandmaster
(GM)
Frequency source
Time
Slave
(S)
Frequency sink
Time Grandmaster
(GM)
Frequency source
Time
Slave
(S)
Frequency sink
Open arrows indicate direction
master  slave (time)
or source  sink (frequency)
Closed arrows indicate
direction of optical waves
WR calibration (cal) channels not needed
if deploying redundant WR links (ie. one WR
link over fiber a and one WR link over fiber b)

## Slide 20: Time network topology
PkN
UTC(kN) +
Primary frequency standard N
kN
UTC(kN)
Single-fiber ELSTAB link
west, GM; east, S
includes amps, muxes,…
Single-fiber WR link
west, GM; east, S
includes amps, muxes,…
k2
S1a
GM
1b
Pk1
GM
1a
S1b
GM
1a
S1a
GM
1b
S1b
S7a
GM
7b
Pk7
GM
7a
S7b
GM
7a
S7a
GM
7b
S7b
S4a
GM
4b
Pk4
GM
4a
S4b
GM
4a
S4a
GM
4b
S4b
S2b
S2a
GM
2b
GM
2a
k3
S3b
S3a
GM
3b
GM
3a
k9
S9b
S9a
GM
9b
GM
9a
k8
S8b
S8a
GM
8b
GM
8a
k6
S6b
S6a
GM
6b
GM
6a
k5
S5b
S5a
GM
5b
GM
5a
XN
ELSTAB endpoint
X = GM, S
XN
WR endpoint
X = GM, S
Non-WR Ethernet link
Local PPS/10 MHz/ToD
Signals ELSTAB (a) and WR (a) travel
through the same fiber. Likewise for
ELSTAB (b) and WR (b)

## Slide 21: Optical frequency network topology
MLS
N
Multi-branch repeater laser station N
RLS
N
Repeater laser station N
Single-fiber ultrastable link
west, source; east sink
RLS
2b
RLS
2a
RLS
3a
compare
MLS
1
RLS
1b
seed
OC1
MLS
4
compare
compare
FW2b
FW2a
OC3
RLS
3b
compare
OC4
MLS
6
RLS
6b
seed
OC6
compare
RLS
1a
RLS
6a
compare
compare
RLS
4a
RLS
4b
FW5a
FW5b
RLS
5a
RLS
5b
compare
compare
compare
compare
compare
seed
RLS
7a
RLS
7b
Flywheel (ultrastable laser) N
Optical clock N
Local link
west, source; east, sink

## Slide 22: C-TFN Timeline
2024: build and Pathfinder link and prepare C-TFN
2025 - 2027: Build TFN Phase 1
After July 2027: TFN Phase 2 (funding not yet identified)
GN5-2 project preparation
2024 (GN5-1)
2025-27 (GN5-2)
C-TFN build, commissioning, operation
Pathfinder link Poznan-Braunschweig
April GN5-2T workplan agreed
Run procurement
Q4 2024
GEANT gate for procurement

## Slide 23: Conclusions
GÉANT is building two fibre routes in the next 3 years:
  France-Belgium-Netherlands-Germany-Poland
  Italy-Austria-Germany-Czechia-Poland
GÉANT has created a new SIG to coordinate collaboration between metrology and NRENs
Funding in place for Jan 2025 to July 2027.
The sustainability working group is actively working with the EC to find funding after 2027

## Slide 24
Thank You
Any questions?
www.geant.org

## Slide 25: Sustainability challenge
GN5-2 2025 to 2027
GN5-3 2027 to 2029
FP10 starts 2028 through to 2034
€2.5 - €7.5 million *
HE funded
GÉANT TF funding
NMI / NREN TF funding
DG-CONNECT
DG-CONNECT
DG-???
Horizon Europe
* Pending governance approval

## Slide 26: Service level hierarchy
GÉANT
NMIs / NRENs
Civil / Commercial / Research
General public
International links
Metrology services
and national links
Large users of metrology services
Individuals using metrology services

## Slide 27
Since 1968 the second has been defined by measurement using Cesium ‘RF’ atomic clocks.
Optical atomic clocks are now a better technology for measuring time
How accurate are atomic clocks?

## Slide 28: Optical clocks need fibre!
In 2022, the 27th CGPM approved Resolution 5 towards the redefinition of the second by 2030 using optical clocks
“Member States to support the development of national and international infrastructures mandatory for optical frequency standard comparisons”
“As of today, only comparisons mediated by optical fibre links provide the required instability and accuracy for comparing optical clocks”
NRENs are really good at this bit!