## Slide 1: Options and considerations for the norther route
Jochen Kronjäger (PTB)
SIG-TFN meeting 23/10/2024

## Slide 2: MLS functionalities (Exail)
„User“
Passive interferometer port for stability assessment
Output frequency offset fixed
Input frequency offset constrained by PD bandwidth
Some functionality may require specific input offset
„Downlink“
Actively stabilised link
Output frequency offset servo-controlled
Input expected at specific offset, e.g. +74 MHz
MLS
„Uplink“
Laser lock to incoming light
Output frequency offset fixed
Uplink ports always works, provided input frequency is within scanning range of internal laser.
Downlink port only works if subsequent stage returns correct frequency offset
User port may not work unless subsequent stage returns correct frequency offset
All ports also provide unfiltered beat notes within constraints of PD bandwidth

## Slide 3: RLS functionalities (Exail)
„User“
Local downlink or passive interferometer port
Output frequency offset fixed
Input expected at specific offset (local downlink only)
„Downlink“
Actively stabilised link
Output frequency offset servo-controlled
Input expected at specific offset, e.g. +74 MHz
RLS
„Uplink“
Internal laser offset-locked to input light
Output frequency offset fixed
Uplink ports always works, provided input frequency is within scanning range of internal laser.
Downlink port only works if subsequent stage returns correct frequency offset
User port may be configured as local downlink or as passive interferometer port
All ports also provide unfiltered beat notes within constraints of PD bandwidth

## Slide 4: Cascading RLS/MLS
uplink
downlink
MLS
MLS
RLS
uplink
downlink
Type -76
Type +74
Type -76
mandatory
mandatory
for full functionality
for full functionality

## Slide 5: Design pattern: one-way chain
MLS
MLS
MLS
RLS
Comparison
Flywheel
No reduncancy: if uplink fails, all downstream locations are cut off
No choice: Only one flywheel is disseminated
Individual link (n→n+1) validation: locally at n
End-to-end link (1→N) validation: requires data of all N locations
Can be implemented using Exail or PSNC equipment
Link validation
Link validation
Link validation
n=1
n=2
n=N
n=…
Note: sequence of MLS/RLS must have alternating „parity“:
+74/−76 MHz for Exail
30/50 MHz for PSNC

## Slide 6: Design pattern: counter-disseminating
Flywheel A
Flywheel B
n=1
n=2
n=N
n=…
Comparison
Comparison
Reduncancy: if one uplink fails, the other one is still functional (albeit not validated)
Choice: Each location can choose from flywheel A or B at any time
End-to-end link (1→N) validation: requires data from both end-point comparators
Individual link (n→n+1) validation: requires additional data from each location (n)
Can be implemented using Exail or PSNC equipment
Note: sequence of MLS/RLS must have alternating „parity“:
+74/−76 MHz for Exail
30/50 MHz for PSNC

## Slide 7: Design patterns are incompatible
MLS
Flywheel
Flywheel B
Comparison
Problem: incoming light has incorrect offset, active compensation will not work
long-distance two-way comparison – not desirable
½ Comparison
½ Comparison
n+1
n
add another RLS
Possible solutions:

## Slide 8: Situation Paris-Lille
Existing Refimeve network (to my knowledge) – unlikely to be fundamentally changed?
MLS
Flywheel
Paris
Lille
RLS
Local use
Current:
Planned:
MLS
Flywheel
Paris
MLS
Lille
+Local use
To Brussels
To London

## Slide 9: Option 1: cascaded MLS Lille→BS
MLS
Lille
Amsterdam
Braunschweig
Brussels
MLS
MLS
RLS
Link validation
Link validation
Link validation
Comparison
Paris-BS
RLS
Comparison
Poznan-BS
Compatible with plans at Lille
Will not work until MLS in place
BS is already a „comparator“ in clock comparisons – little extra effort for additional data uploads
Beat frequency well defined
Beat frequency arbitrary

## Slide 10: Option 2: cascaded MLS BS→Lille
MLS
Braunschweig
Brussels
Lille
Amsterdam
MLS
MLS
RLS
Link validation
Link validation
Link validation
Comparison
Paris-BS
RLS
Other local comparison
Two-way
Compatible with existing situation at Lille
Needs extra RLS at Lille
Lille must become a „comparator“ – feasible outside an NMI?
Beat frequency well defined
Beat frequency arbitrary

## Slide 11: Option 3: counter-disseminated flywheels
Flywheel
Flywheel
Comparison
Comparison
Braunschweig
Amsterdam
Brussels
Lille
Paris
Would likely require new equipment at Lille
Existing RLS/MLS could be utilised
Would likely require new fibre all the way to Paris
Therefore unlikely?

## Slide 12: One-way chain: building blocks
Any NMI with two next neighbours can choose one of the following, and the chain will work:
MLS
Link validation
„Chain link“
„Stop and go“
Two-way
comparison
„Pass-through“
Local use (active/passive)
Local use (active/passive)
Local use (active/passive)
RLS
RLS
Benefit: two redundant flywheels
Obligation: share data („comparator“)
Possible only once in a link between flywheels
Caution: only work within the „one-way chain“ context
Requires accurate 10 MHz (< 10-13)

## Slide 13: Option 4a: evolution Lille-Braunschweig #1
MLS
Braunschweig
Brussels
Lille
Amsterdam
MLS
RLS
Link validation
Link validation
Comparison
Paris-BS
RLS
Other local comparison
Two-way
Works even without any connection in Lille
Interim connectivity to Poznan, Paris, Turin, (London) through Braunschweig - Strasbourg
Requires accurate 10 MHz (< 10-13)

## Slide 14: Option 4b: evolution Lille-Braunschweig #2
MLS
Braunschweig
Brussels
Lille
Amsterdam
MLS
Link validation
Link validation
Once ready (MLS at Lille, FXE at Amsterdam),
Switch direction of Brussles MLS
Rearrange RLS at Amsterdam from „pass-through“ to „stop-and-go“
Amsterdam becomes „comparator“
Two-way
comparison
Local use (active/passive)
RLS
RLS
MLS
Link validation
Requires accurate 10 MHz (< 10-13)

## Slide 15: Critical featurs of option 4b
Compatible with Refimeve (assuming MLS at Lille)
Only one MLS ever needed at Brussels
Choice and redundancy at Amsterdam
One additional „comparator“ between Braunschweig and Paris
Is it possible to have 1-3 and avoid 4?

## Slide 16
Amsterdam
Braunschweig
Fibre 1
Fibre 2
NIRP Laser
Brussels
Fibre 1
Fibre 2
LILLE
MLS
MLS/RLS
MLS/RLS
Fibre 1
Fibre 2
MLS/RLS
MLS/RLS
MLS/RLS
MLS/RLS
Original slide by Krzysztof Turza
No extra comparator, but validation of link requires comparison at Braunschweig and Brussels, plus data sharing.
Requires additional MLS/RLS at Brussels.
Comparison
Comparison
The combination of „one-way chain“ and „counter-disseminating“ patterns is made possible through an extra MLS/RLS at Brussels.

## Slide 17
MLS
Lille
Amsterdam
Braunschweig
Brussels
MLS
Paris
RLS
30
RLS
50
UL
DL2
AUX
DL1
UL
AUX
DL1
RLS
30
RLS
50
UL
AUX
DL1
UL
AUX
DL1
Comparison
With material by Krzysztof Turza
and inspired by Jeroen Koelemeij
Requires PSNC equipment at Amsterdam and Braunschweig, plus a few extra AOMs between Amsterdam and Brussels.
One full chain Lille-Braunschweig, plus second (short) chain Braunschweig-Paris.
Both separately conform to „one-way chain“ design pattern.

## Slide 18: Flywheel considerations
We want actively phase-compensated links in order to minimise the need to share data outside the comparator concept, and to provide users wih a physical ultrastable signal everywhere.
Concept of comparators: one party is responsible for producing and sharing one physically meaningful frequency ratio/difference, see Lodewyck 2020 https://doi.org/10.1103/PhysRevResearch.2.043269
This is especially true in the initial phase, where few NMIs will have good flywheels, and where the data infrastructure will not yet be available.
Flywheels must meet specs e.g. to make sure beat frequencies stay within bandwdith constraints:
  Frequency within, say , 100 MHz of 194.4 THz (could be substantially more)
  Drift less than 2 mHz/s (Counter sync to 1 ms) or 2 Hz/s (counter sync to 1 us)
  Instability less than…
  Uptime…