## Slide 1: Establishment of an optical fibre link between NPL and Birmingham University for the purpose of Time & Frequency dissemination
Jacques-Olivier Gaudron
Fibre Links Team (Wei Huang, Namneet Kaur, Reinhard Karembera, Alex Korwin)
GEANT SIG-TFN technical WG
26th July 2024

## Slide 2: Agenda
Introduction & Purpose
Setup and signals on the link
Link optimisation
Link monitoring
Conclusion and future work

## Slide 3: Introduction & purpose
Research: Currently NPL is developing optical atomic clocks, but these are only compared with European partners on a sporadic basis.
  > Need for more distributed development and ability to compare clocks more regularly, particularly in light of the SI second redefinition.
Infrastructure: Resilience > GNSS is vulnerable to external threats such as Jamming, Spoofing, Meaconing but also environmental changes. All these are discussed in detail in the Blackett review. Optical fibre links are one way of building resilience in T&F dissemination.
Future Industry: The current Frequency standard based on Caesium fountains has a performance that is at least 1 order of magnitude worse than Optical atomic clocks, interest in WR, PTP.

## Slide 4: 1. Geographical Overview
CONFIDENTIAL
2 dark fibres
6 colocations sites located every 40 to 60km with selective filtering (DWDM) and bidirectional amplification
Overall fibre length: ~ 380km

## Slide 5: 1. Signals on the link
Signals share a single fibre based on Dense Wavelength-Division Multiplexing (DWDM) technique.
Seismic detection & environmental
monitoring
NPLTime®
Optical carrier
UTC(NPL) 1PPS
& 10MHz
Time of day via
White Rabbit
Monitoring

## Slide 6: 1. Setup
ELSTAB 10MHz & 1pps from MASER
@channels 39 to 42
Management (control of equipment along link)
@ channels 73 to 99
L-Band
Laser source
@ channel 7
Network Switch & Optical amplifiers
Wavelength division
multiplexing
C-Band Ultra-stable laser
@ channel 44
Wavelength
division DE-multiplexing
REMOTE ELSTAB 10MHz & 1pps @channels 39 to 42
Management (control of equipment along link) @ channels 73 to 99
L-Band
Laser signal @ channel 7
C-Band Ultra-stable laser signal @ channel 44
Network Switch & Optical amplifiers
Spans
Housed
at NPL
Co-locations
Housed at
University
of Birmingham
Pair of optical fibres (length c. 380km x 2)
Note: The term channel is widely used in the telecoms industry to refer to a particular wavelength of light, it is standardised by the ITU
(International Telecommunications Union) standards

## Slide 7
N_In
N_+1_Out
ByPass_Out
ByPass_In
User_Out
N_In
N_+1_Out
ByPass_Out
ByPass_In
User_Out
Beat_User_Out
Fibre length c. 5m
Fibre B (or 2) MONITORING
Overall length c. 380km
N+1 Fibre link
Fibre A (or 1) DISSEMINATION Overall length c. 380km
75MHz
BP filter
RF Amplifier
T1 Laser locked to 1064nm ultrastable cavity via Comb
RLS
74MHz
(B’ham)
RLS
76MHz
(NPL)
Reading
ELSTAB
amplifier
Studley
ELSTAB
amplifier
Amplifiers & spans
Reading
Keopsys
amplifier
Studley
Keopsys
amplifier
User in Birmingham
1. Setup (OC only)
Notes: Here I am using RLS because I had this slide before and want to keep simple

## Slide 8: 2. DWDM allocation
Beyond Reading | Fibre 1 or A | Fibre 2 or B
Ch. # / λ nm | OBA-3 | Keopsys
38 / 1546.92 |  | 
39 / 1546.12 | ELSTAB Monitoring | 
40 / 1545.32 | ELSTAB Dissemination | 
41 / 1544.53 | ELSTAB Dissemination | 
42 / 1543.73 | ELSTAB Monitoring | 
43 / 1542.94 | Seismic Beppe | Seismic Beppe
44 / 1542.14 | OC Dissemination | OC Monitoring
45 / 1541.35 | White Rabbit Dissemination | 
46 / 1540.56 |  | White Rabbit Monitoring
47 / 1539.77 |  | 
48 / 1538.98 |  | 
Amplifier passband | Amplifier stopband

## Slide 9: 2. Installation status
Reading
Froxfield
Chippenham
NPL
Bradley Stoke
B’Ham
Gloucester
Studley

## Slide 10: Link monitoring
Remote monitoring and control GUI for:
OBA-3 amps
Keopsys amplifier
ELSTAB modules
Spectrum Analyser
Scope to add
instruments in future.
Log file keeping a record of faults, uptime etc.
Note: All remotely connected devices are interrogated every 15 minutes, and all data is saved in the server.
In case of fault an email is sent with details of location.
!!! Recent fault (broken fibre) was detected within 3 mins and fixed the same day.

## Slide 11: Link monitoring
Status of EDFAs on link
Amplifier parameters
Run commands if you INSIST on using Shell…
Tab Menu
Menu Bar
Configuration options
Time of last query for selected amplifier
Close software, stop monitoring threads
Monitoring options

## Slide 12: Link monitoring (OFDR*)
*Optical Frequency Domain Reflectometry
Sawtooth generator now controlled by a SDR (Software Defined Radio)
Frequency
Modulated signal
Spectrum Analyser signal

## Slide 13: Link performance 7th to 15th June 2024
Up times
ELSTAB: 99.97%
White Rabbit: 98.63%
Optical carrier: 96.71%
Notes: WSI for White Rabbit? Signal reflection in Fibre A? Interference?

## Slide 14: Conclusion and future work
Work done: T&F signals are ready to use via London-Birmingham link:
  Optical Carrier (OC) > Syntonisation
  ELSTAB > Synchronisation once calibrated
  White Rabbit > Time of day
Future work:
  Devise method for gain optimisation for both OC & ELSTAB
  Upgrade hardware for White Rabbit
  Build a small form factor OFDR
  Real-time calibration on 1 PPS signals
  L band optical carrier distribution (on Ch7), enabling use of Dark Channels
  And more