## Slide 1: Potential International Time and Frequency Network Topologies
Discussion document - open for comments and suggestions
Jeroen Koelemeij (VU Amsterdam)
v2 – August 7, 2024

## Slide 2: Contents
Notes on Sagnac effect
Wavelength plan
Wavelength considerations
Amplifiers and repeaters
Time network topology
Time network considerations
Optical frequency network topology
Optical frequency network with output frequency steering of flywheel
Optical frequency network considerations

## Slide 3: 1. Notes a priori on Sagnac effect
Sagnac effect caused by Earth’s rotation enters in various ways:
  When comparing the phase of two opposing optical waves travelling through a rotating fiber loop with enclosed area A [1]  source of nonreciprocal frequency noise in large loops
  In linear fiber links, when time-synchronizing clocks with nonzero east-west distance (Sagnac delay proportional to area AE obtained by equatorial projection of vector tracing the fiber path between the endpoints) [2]
    Sagnac time delay of several nanoseconds on European length scales
    Sagnac delay can be up to 10-6 relative to fiber delay: implied nonreciprocal noise in stabilized optical fiber links?
  Needed: automated Sagnac calculator that takes all these contributions into account (especially the contribution by AE)
    [1] See e.g. Clivati et al., Opt. Lett. 38, 1092 (2013)
    [2] See e.g. Sliwczynski et al., Metrologia 50, 133 (2013)

## Slide 4: 2. WDM wavelength plan for TF signals (lambdas TBD)
ELSTAB Tx
ELSTAB Rx
WR Tx
WR Rx
MUX
Optical fiber b
WR Tx Cal
WR Rx Cal
CH44 ultrastable
optical carrier
ELSTAB Rx
ELSTAB Tx
WR Rx
WR Tx
WR Rx Cal
WR Tx Cal
CH44 ultrastable
optical carrier
MUX
ELSTAB Rx
ELSTAB Tx
WR Rx
WR Tx
MUX
Optical fiber a
WR Rx Cal
WR Tx Cal
CH44 ultrastable
optical carrier
ELSTAB Tx
ELSTAB Rx
WR Tx
WR Rx
WR Tx Cal
WR Rx Cal
CH44 ultrastable
optical carrier
MUX
Fiber pair
Time Grandmaster
(GM)
Frequency source
Time
Slave
(S)
Frequency sink
Time Grandmaster
(GM)
Frequency source
Time
Slave
(S)
Frequency sink
Open arrows indicate direction
master  slave (time)
or source  sink (frequency)
Closed arrows indicate
direction of optical waves
WR calibration (cal) channels not needed
if deploying redundant WR links (ie. one WR
link over fiber a and one WR link over fiber b)

## Slide 5: 3. Wavelength considerations
Ultrastable optical frequency transfer
  Ch 44 (1542.14 nm): de facto standard for ultrastable optical frequency transfer in Europe; widest choice in COTS equipment
ELSTAB
  Suited for in-band transmission coherent DWDM system? Guard bands needed?
WR (1.25 Gb/s OOK)
  Can operate at any wavelength for which Gigabit Ethernet SFPs are available
  In-band transmission via coherent DWDM systems: risk of channel cross talk, guard bands needed?
  Out-of-band operation: OSC band near 1511 nm. Disadvantage: SFPs with wavelengths on 100-GHz DWDM grid near 1511 nm not generally available (but have been produced in the past)
  Prefer ‘wavelength-locked’ DWDM SFPs over CWDM SFPs: DWDM SFPs have smaller wavelength drift  less nonreciprocal delay variation due chromatic dispersion (typically < 0.1 ns for a 100 km link [1])
  DWDM SFPs with slightly tunable wavelength (via I2C) are commercially available (nice-to-have, could be useful for chromatic dispersion calibration)
Before a wavelength plan is decided on, the chromatic dispersion calibration procedures for time links must have been selected (and tested, if procedure not part of current state of the art)
  Chromatic dispersion can be tested by varying wavelength over known amount (e.g. 0.08 nm) and measuring delay difference, or by swapping Tx and Rx wavelengths on both ends of a link
  [1] C. van Tour and J.C.J. Koelemeij, ngVLA Memo #22 (2017) library.nrao.edu/public/memos/ngvla/NGVLA_22.pdf

## Slide 6: 4. Amplifiers and repeaters
Amplification: EDFAs for ultrastable optical frequency and ELSTAB
  Separate or shared amplifiers?
  Gain limited to ~20 dB (bidirectional operation)
WR: OEO repeater
  Cost-effective: SFP media converter + two SFPs
  Gain  Rx sensitivity  35 dB possible
  Performance in terms of added jitter as good as optical amplifier
  Minor disadvantage: wavelength drift of DWDM SFPs in OEO  slight additional nonreciprocal delay variations due to chromatic dispersion
WR alternative: EDFA or SOA
  More expensive than OEO
  SOA: bidirectional transmission of OOK signals can lead to cross talk via cross-gain modulation (XGM)
  Using WDM filters and quasi-bidirectional amplifiers (two anti-parallel unidirectional amps) maximum amplifier gain (30-35 dB) attainable and XGM avoided (in case of SOAs)

## Slide 7: 5. Time network topology
PkN
UTC(kN) +
Primary frequency standard N
kN
UTC(kN)
Single-fiber ELSTAB link
west, GM; east, S
includes amps, muxes,…
Single-fiber WR link
west, GM; east, S
includes amps, muxes,…
k2
S1a
GM
1b
Pk1
GM
1a
S1b
GM
1a
S1a
GM
1b
S1b
S7a
GM
7b
Pk7
GM
7a
S7b
GM
7a
S7a
GM
7b
S7b
S4a
GM
4b
Pk4
GM
4a
S4b
GM
4a
S4a
GM
4b
S4b
S2b
S2a
GM
2b
GM
2a
k3
S3b
S3a
GM
3b
GM
3a
k9
S9b
S9a
GM
9b
GM
9a
k8
S8b
S8a
GM
8b
GM
8a
k6
S6b
S6a
GM
6b
GM
6a
k5
S5b
S5a
GM
5b
GM
5a
XN
ELSTAB endpoint
X = GM, S
XN
WR endpoint
X = GM, S
Non-WR Ethernet link
Local PPS/10 MHz/ToD
Signals ELSTAB (a) and WR (a) travel
through the same fiber. Likewise for
ELSTAB (b) and WR (b)

## Slide 8: 6. Time network considerations
Purpose: strictly for comparisons, i.e. there is no physical ‘grandmaster network time’
  Only distinction made is between UTC(k) sites with and without primary frequency standards
  Any ubiquitous time scale is virtual (cf. paper time scale), with physical realizations generated only locally by designated laboratories
All time links have (practically) zero enclosed area  only ‘east-west’ Sagnac delay needs be taken into account
Sites with primary frequency standards directly compared via high-stability, high-accuracy ELSTAB system
  High stability and accuracy for an optimal connection between TAI and SI second (future: ultrastable optical frequency links and SI second based on optical clocks)
  ELSTAB sites form high-accuracy pivot points to assess ‘end-to-end’ (or rather pivot-to-pivot) accuracy and stability of WR links (and other TF transfer methods, including satellite)
Redundant fiber pairs with opposite ELSTAB time flows:
  If connected to at least two neighbors under nominal conditions, at least one connection to neighbor remains available in case of a fiber break
  Two-way monitoring of link performance & determination of ‘east-west’ Sagnac delay (practically zero enclosed area)
Nearest-neighbor comparisons via WR
Redundant fiber pairs with opposite WR time flows:
  Redundancy: a given UTC(k) site will be connected to at least one neighbor in case of fiber break, and to at least two neighbors
  Two-way monitoring of link performance & determination of Sagnac delay
Segmented GM-S WR links may be networked together via local non-WR Ethernet links

## Slide 9: 7. Optical frequency network topology
MLS
N
Multi-branch repeater laser station N
RLS
N
Repeater laser station N
Single-fiber ultrastable link
west, source; east sink
RLS
2b
RLS
2a
RLS
3a
compare
MLS
1
RLS
1b
seed
OC1
MLS
4
compare
compare
FW2b
FW2a
OC3
RLS
3b
compare
OC4
MLS
6
RLS
6b
seed
OC6
compare
RLS
1a
RLS
6a
compare
compare
RLS
4a
RLS
4b
FW5a
FW5b
RLS
5a
RLS
5b
compare
compare
compare
compare
compare
seed
RLS
7a
RLS
7b
Flywheel (ultrastable laser) N
Optical clock N
Local link
west, source; east, sink

## Slide 10: 8. Optical frequency network topology w/ steering
MLS
N
Multi-branch repeater laser station N
RLS
N
Repeater laser station N
Single-fiber ultrastable link
west, source; east, sink
Local link
west, source; east, sink
RLS
2b
RLS
2a
RLS
3a
compare
RLS
1b
seed
OC1
MLS
4
compare
compare
FW2b
FW2a
OC3
RLS
3b
compare
OC4
RLS
6b
seed
OC6
compare
RLS
1a
RLS
6a
compare
compare
RLS
4a
RLS
4b
FW5a
FW5b
RLS
5a
RLS
5b
compare
compare
compare
compare
compare
seed
RLS
7a
RLS
7b
Flywheel (ultrastable laser) N
Optical clock N
AOM
MLS
1
steering 1
AOM
steering 2b
AOM
steering 6
MLS
6
AOM
Steered acousto-optic modulator N

## Slide 11: 9. Frequency network considerations
Purpose: strictly for comparisons, i.e. there is no ubiquitous ‘reference frequency’
  Distinction between sites with optical atomic clock (OC) with or without MLS, and flywheel ultrastable laser
  Any ubiquitous reference frequency would virtual (cf. paper time scale), with physical realizations generated only locally by designated laboratories
  Concept of virtual or ‘paper’ reference frequency does not yet exist, but would technically be feasible
Redundant fiber pairs with opposite frequency flows:
  If connected to at least two OCs under nominal conditions, at least one connection to OC available in case of fiber break
  To-way monitoring of link performance
  Practically zero enclosed area, so practically no Sagnac frequency noise (except for negligible(?) nonreciprocal noise due to east-west relative delay asymmetry of order 10-6)
If closed loop, Sagnac phase could be determined by differencing cumulative phases in clockwise and counter-clockwise directions
Without AOM steering: flywheel sites could use post-correction data to maintain traceability to SI second of neighboring OC
With AOM steering:
  Frequency-lock to neighboring MLS (and effectively copy SI second realization from typically a different nation in real time)
  Or use AOM for steering to virtual reference frequency/virtual SI second
OC sites can also use AOM steering to produce virtual SI second