## Slide 1
Beyond eduroam
Progress @ SURF of mobile related developments

## Slide 2: Spin-offs talk @ mobility day
Goal: to share our ideas quickly and activities, find ground to collaborate:
Private 5G
IoT stuff
eVA
govroam
From eduroam to SURFwireless to CNaaS

## Slide 3: Title slide
Private 5G

## Slide 4: What is private 5G? And why should NRENs care?
Dedicated Spectrum: Runs on licensed, unlicensed, or shared spectrum depending on country regulations.
Self-owned and controlled RAN: Institutions can install their own radio access network (RAN), operated independently or in collaboration with a telecom provider
What:
Improved availability of the access network
Enabling specific use cases: critical communications, specific demands
Use the SIM to grant access to eduroam (couple 5G core to RADIUS)
Data sovereignty
Economical alternative for indoor cellular solutions of public telecom providers
Why:

## Slide 5: Multi-operator & multi-campus solution for indoor 5G

## Slide 6: 5G and Wi-Fi access networks at a glance
5G
Uses licensed spectrum in 0.7, 0.9, 1.8, 2.1, 2.6, 3.5, 60 GHz; NO interference
Includes both access and core facilities
Network instructs devices what to do
Focus on outdoor usage with a range of 2-10 km
High cost for setup; requires a mobile plan with a data subscription
Authentication : SIM card
Offered limited operators per country (Private 5G may change this)
Wi-Fi
Uses unlicensed spectrum in 2.4, 5, 6 GHz; little coordination; expect interference
Restricts to an access network facility
Client devices decides on all radio actions
Focus on indoor usage with a range of 100m
Easy deployment in homes and offices; eduroam subscription service
Authentication: password or username+password
Implemented in every home, office and institution

## Slide 7: Private 5G: Current situation & next steps
SURF’s private 5G network: operational in open source ‘extended lab setting’ Multiple implementations of radio access networks & core networks
Use the SURF 5G infrastructure to explore:
  Possibilities to integrate private and public 5G networks
  Using the SIM to authenticate to eduroam

## Slide 8: RAN sharing with telecom providers
Key challenges:
  Radio Resource Management and Orchestration How to manage radio resources (e.g., spectrum, power, scheduling) across multiple administrative domains
  Coordination between different domains to ensure fairness, security, and performance
Considerations:
  RAN slicing
  Spectrum sharing, dynamic resource adaptation, use slices for separate adminstrative domains
  Sharing of virtual network and compute functions in the RAN
  Apply multi-tenant containerization technologies in the RAN to separate administrative domains
  Abstract virtualized RAN services and offer to each domain via a set of APIs or orchestrated service offerings
  Edge computing and local breakout for each domain
  Solution depends on desired level of isolation, operational flexibility, and cost-efficiency

## Slide 9: Screenshot of phone connected to SURF’s 5G network
Mobile
country
code NL
Mobile
network
code SURF
Private frequency used for 5G
Stand alone 5G (no 4G legacy)
5G radio details

## Slide 10: eVA
What about all those campus visitors without eduroam?
Service: eduroam Visitor Access is now “the standard” in NL-education for visitors;
Developments:
  We provide eVA to a few other NRENs “as a service”
  Bug fixing
  SMS reliability also for outside numbers

## Slide 11: iotroam
What to do with Wi-Fi devices that cannot do 802.1x (or user’s don’t want to use their credentials on shared iot devices)
This means paperwork for the network administrator 
Request for solution: an eduroam for iot devices
Vendor neutral solution is preferred (to prevent vendor lock in)
iotroam: self-built software that couples MAC addresses with unique credentials
Operational since January 1st 2025. Included in the basic tariff.

## Slide 12: iotroam

## Slide 13: Fast growth…

## Slide 14: But… what with sensors without wifi?
Users: “We want something like eduroam for non-wifi low powered devices”
… and something to store their data, visualize it, etc.
Idea: to provide managed LoRaWAN on each institute.
Why? Cooperation between institutes to embrace techology and develop use cases on a similar manner
Use ChirpStack LoRaWAN server
Optional: provide storage, visualization

## Slide 15: LoRaWAN + SURF Research Cloud
LoRaWAN
Gateways
Sensors
Network server
SURF service in development
Catalogue item in SURF Research Cloud
Other networks, like SkyNet or TTN

## Slide 16: Govroam NL
In 2014, govroam foundation NL was started to provide govroam to Dutch governments
Now, In 2025, the govroam foundation delivers:
  govroam almost all big government institutes (and many of the smaller)
  getgovroam
  govguest
  govVPN
  govGain

## Slide 17: SURFwireless: a success story leading to disruptive innovation?
SURF Wifi as a Service Since 2016
Current status (2025):
30 institutes
300+ locations
Approx 11.000 AP’s

## Slide 18
Developing Campus as a Service portfolio (CNaaS)
Wi-Fi as a Service successful, but additional services are required to be useful for institutes
SURF strategy: creating a CNaaS service portfolio, connecting users and (their) devices in a secure and user-friendly manner to local or worldwide resources.
Connection type: wired, wireless, low powered, mobile, cloud, …
What we do: Managing wireless, wired, router, firewall, DHCP, DNS, NAC, ...
All-inclusive: Procurement, installation, management, support, maintenance. Directed by SURF, together with market and institute
BoF session about CNaaS cooperation: Wednesday at 11!
18
Notes: 18

## Slide 19
NRENs should cooperate more in campus infrastructure
(agree or disagree?)

## Slide 20
Thanks
Maurice van den Akker
www.surf.nl